## Slide 1: wueHans: A Full-Stack Open-Source RISC-V Gaming Console and SoC Architecture
Yannik Stamm, Jonathan Hager, Timo Grundheber, Matthias Jung and Sebastian von Mammen
11.06.2026
Notes: Slide danach mit Spielekonsole, die schon existiert und dazu die einleitenden Worte

## Slide 2: Different consoles
[7]
[8]
We've built our own!

## Slide 3: Progress of our console
2023
2025
  Move to open source RISC-V core
  FPGA-based
  Custom GPU
  3D-printed case
  Selfmade CPU with custom ISA
  FPGA-based
  Adapted vasm backend [6]
  Custom linker and loader

## Slide 4: Console Architecture
  50 MHz VexRiscv
  4 kB I- and D-cache
  400x240 sprite-based GPU
  32 kHz, 16-bit audio
  32 kB SRAM
  32 MB SDRAM
  Game input with two SNES controllers
  ELF format supported by the bootloader

## Slide 5: RISC-V CPU
Address | Name
0x00000000 | SDRAM
0x02000000 | GPU
0x02000100 | Audio
0x02000200 | Controller
0x02000300 | Counter
0x02002000 | Color table
0x02010000 | Bootloader
0x80000000 | SD-Card
  VexRiscv (CPU) [5]
    many alternatives, e.g., Neorv, picorv, ...
  ISA extensions:
    Rv32imf
    Hardware floating-point support
  Open-Source design
  Memory-mapped registers for
    GPU
    Audio
    ...

## Slide 6: Sprite-Based GPU
imageWidth
(screenX, screenY)
width
(xOffset, yOffset)
height
imageStart
Notes: + Tabelle ausm Wiki. Gibt Daten, Befehle, ...

## Slide 7: Sprite-Based GPU
Rectangle is created
Address of the desired pixels is computed
Data is fetched from the AXI Bus
Images only store indices to a color table. The correct colors are fetched
The final pixels are written to the framebuffer
Notes: 1-5 animieren

## Slide 8: Audio System

## Slide 9: Prototype

## Slide 10: Prototype
[1]
  Lattice ECP5 with 84k LUT
  32 MB SDRAM
  Micro-SD slot (to store the game)
  Digital video output
  25 MHz clock
Notes: Daten zum FPGA

## Slide 11: Prototype - Controller
[2]
[1]
3.3 V
5 V
Level shifter
Notes: Boxen über die Bilder

## Slide 12: Prototype - Audio
Digital-Analog converter
Amplifier
Speakers
Notes: Boxen mit Aufgabe der Platinen

## Slide 13: Prototype - Case

## Slide 14: Prototype - "Workstation"

## Slide 15: Prototype

## Slide 16: EDA Tools & Software
EDA Tools:
  Simulation: Icarus Verilog, GTKwave and Surfer
  Synthesis: Yosys, nextpnr, fujprog
  All tools bundled in the oss-cad-suite [3]
  Build system with CMake for hardware and software
Software:
  Support for C and C++ with the newlib [4] standard library
  Virtual prototype for testing and debugging
  Hardware Abstraction Library
  Software template that can be used to quickly start developing
  Bootloader
Notes: Screenshot von einem Tool

## Slide 17: Game Jam
  One weekend spent at the university
  High interest especially of Games-Engineering students
  Low barrier of entry for any game developer

## Slide 18: Current Games
Hans Tower Defense
Hans The Gatherer
Cow Shooter
Hans Tennis

## Slide 19: Current Games
Hans Tower Defense
Hans The Gatherer
Cow Shooter
Hans Tennis

## Slide 20: Current Games
Hans Tower Defense
Hans The Gatherer
Cow Shooter
Hans Tennis

## Slide 21: Current Games
Hans Tower Defense
Hans The Gatherer
Cow Shooter
Hans Tennis

## Slide 22: Current Games
Hans Tower Defense
Hans The Gatherer
Cow Shooter
Hans Tennis

## Slide 23: Next Steps
  Improve the audio
  Multicore RISC-V core
  Extend our GPU to handle 3D
  2nd Game Jam
  Integrate everything on a single PCB
  Tapeout with the IHP Open-Source PDK

## Slide 24: References
ULX3S. (2026, May 27). Retrieved from https://radiona.org/ulx3s
Behance. (2019). SolidWorks | SNES Controller - Aonghus Quinn. Behance. Retrieved from https://www.behance.net/gallery/74554165/SolidWorks-SNES-Controller?locale=de_DE
oss-cad-suite. https://github.com/YosysHQ/oss-cad-suite-build
Newlib. https://sourceware.org/newlib/
VexRiscv. https://github.com/SpinalHDL/VexRiscv
vasm. http://sun.hasenbraten.de/vasm/
Martin Iturbide. https://commons.wikimedia.org/wiki/File:Nintendo_Gamecube_Silver.JPG (GNU FDL, unmodified)
Evan-Amos. https://commons.wikimedia.org/wiki/File:Nintendo-Switch-wJoyCons-BlRd-Standing-FL.png